## Slide 1: Applied Artificial Intelligence Lecture 16 Applied AI in industry
Arthur Kordon
Kordon Consulting LLC

## Slide 2: Lecture 16 agenda

## Slide 3: What are the specific features of applied AI in manufacturing

## Slide 4: Lecture 16 agenda

## Slide 5: What are the key features of manufacturing data

## Slide 6: Lecture 16 agenda

## Slide 7: Industry 4.0 or The Fourth Industrial Revolution
Industry 4.0 includes cyber-physical systems, the Internet of things, cloud computing and cognitive computing. Industry 4.0 is commonly referred to as the fourth industrial revolution.
Industry 4.0 fosters what has been called a “smart factory.” Within modular structured smart factories, cyber-physical systems monitor physical processes, create a virtual copy of the physical world and make decentralized decisions. Over the Internet of Things, cyber-physical systems communicate and cooperate with each other and with humans in real-time both internally and across organizational services offered and used by participants of the value chain.

## Slide 8: Digital twins
https://www.ge.com/digital/applications/digital-twin
GE is General Electric

## Slide 9: Digital twins' applications
https://www.ge.com/digital/applications/digital-twin

## Slide 10: Digital twins for wind turbines applications
Digital Twins of wind turbines allow to reduce maintenance costs by:
· Reducing the number of visits to the wind farm;
· Fixing broken parts instead of buying new ones;
· Providing a root cause analysis on component level (when, how, where and why it will fail).
Digital twins allow you to streamline maintenance schedules, power distribution, and load balancing for wind turbines, specifically.

## Slide 11
Emulators based on neural networks
Empirical emulators representing physical assets
Emulators based on genetic programming

## Slide 12: Digital twins vs. empirical emulators
Expensive
First-principles-based
Reliable
Re-usable
Low cost
Data-based
Unreliable
Asset-specific

## Slide 13: Lecture 16 agenda

## Slide 14: Empirical emulators for intermediate products optimization – business problem
A significant problem in the chemical industry is the optimal handling of intermediate products. Of particular interest are cases where intermediate products from one process can be used as raw materials for another geographical location. The project is based on a real industrial application of intermediate product optimization between two plants, one in Freeport, Texas, and the other in Plaquemine, Louisiana.
Current optimization is based on a first-principles model with over 1500 reactions and more than 200 species. The experience of using a vast fundamental model for “what-if” scenarios in planning the production schedule was not favorable because of the specialized knowledge required and the slow execution speed (~20-25 min/prediction).
Key hypothesis: An improved intermediate products handling, based on fast optimization in real-time can have an expected impact of S1.2 million on both plants
Business problem
Project objectives:
Maximize product flow from the plant in Texas and to use it effectively as a feed to the plant in Louisiana
Develop empirical models that emulate the existing fundamental model with acceptable accuracy
The calculation time of the developed models to be < 1 second

## Slide 15: Emulator for optimization of an industrial chemical process
Applied for PER/TET
Optimization at Plaquemine
Inferential Sensors
y = f(x)
Emulators
Symbolic
Regression
Emulator
5 ms/
prediction
Test
Data set
Reactor
Model
20-25 min/
prediction
12 outputs
Four levels DOE
Training
Data set
Unsuitable for online process optimization
10 inputs
Suitable for online process optimization
1.2 MM
EBIT/year
> 9 MM EBIT
COD prediction at Harbor Beach WWTP
2004 - >40 days out of compliance
2005 - ~20 days out of compliance
2006 - 0 days out of compliance
2004
4
2005
5
2006
6
2007
10
Dow Biotech - 3
LHC7 -1
NOx emissions – 5
Plaquemine 2, LaPorte - 3
Harbor Beach - 2
EOEG Fort -2
Train4/5 BSL – 1
Acrylic Acid - 1
POPG Freeport - 10
Reactor
Model
20-25 min/
prediction
10 inputs
12 outputs
Four
levels DOE
Training
Data set
Test
Data set
Symbolic
Regression
Emulator
5 ms/
prediction
On-line process
optimization
$1.2 million/year
reduced cost
Very complex reactor model with slow execution time
Emulator is a simple nonlinear equation

## Slide 16
16
Empirical emulators for intermediate products optimization:
Model generation/validation by neural networks
Selected neural network models for each product
Y5 neural net model performance on test data

## Slide 17
17
Empirical emulators for intermediate products optimization:
Model generation/validation by genetic programming
Genetic programming-generated model for Y5 product
Y5 genetic programming model performance on test data

## Slide 18
18
Empirical emulators for intermediate products optimization:
Off-line optimization by Excel Solver

## Slide 19: Lecture 16 agenda

## Slide 20: What are Inferential sensors
20
143.0 ppm
Training
data
Models generated by Genetic Programming
Simple
formulas
Easy On-Line
implementation
Inferential Sensor
An empirical model based on analytical equations with built-in self-assessment capability
Key objective:
To predict difficult-to-measure parameter (emissions) from easy-to-measure data (temperature, pressure, flow, etc.)
Hardware analyzers cost > $250,000

## Slide 21
Models you can understand
Models are robust & trustworthy
Better extrapolation
(low maintenance cost)
Easy on line implementation
(low deployment cost)
Technical advantages of inferential sensors generated by Genetic Programming
The alternative
Continuous Emissions Monitoring Systems (CEMS)
Average cost > $100,000

## Slide 22: Inferential sensors leveraging at Dow Chemical
22
Mature technology pioneered at Dow
- Applied since 1997
200+ applications
30+ processes
+ million$ value
Chemical reactor
Distillation column
Waste Water Treatment Plant
Biomass
Notes: 22

## Slide 23
Using inferential sensors in periods where critical hardware sensor is not available
Critical sensor not available
Critical sensor broken/not available
Critical sensor available
Broken critical sensor

## Slide 24: Lecture 16 agenda

## Slide 25: Automated operating discipline for consistent plant operation in a large-scale chemical plant – business problem
Existing operating discipline process is very sensitive to human errors, competence, inattention, or lack of time.
A specific problem for automated operating discipline is to help plant operators to troubleshoot the complex root causes of upsets
The proposed real-time system captures existing process knowledge on using alarm troubleshooting in establishing a consistent operating discipline in handling difficult process conditions
Key hypothesis: Automated operating discipline, based on an intelligent system in real time can reduce significantly process upsets and have an expected impact of Sxxxxxxx
Business problem
Project objectives of the developed Automated Operating Discipline system:
Automatically identify root causes of complex alarms
Provide proper advice to the operator for the root cause of the alarms in real time
Streamline operating discipline through automatically linking the corrective actions to the identified problems
Assist the training of new operators to detect problems and carry out corrective actions
Be easy to operate and maintain
Be open to future changes of alarm logic and corrective actions

## Slide 26
Neural networks
Automated operating discipline for consistent plant operation in a large-scale chemical plant: integrating several applied AI technologies
Genetic programming
Expert systems
Fuzzy logic
Applied AI

## Slide 27
27
Automated operating discipline for consistent plant operation in a large-scale chemical plant – Step1: Building alarm logic diagrams
Alarm logic diagrams integrate expert’s knowledge with process data and developed models

## Slide 28
28
Automated operating discipline for consistent plant operation in a large-scale chemical plant – Step2: Integrating and validating all alarm logic diagrams

## Slide 29
29
Automated operating discipline for consistent plant operation in a large-scale chemical plant – Step3: System deployment and operators training

## Slide 30
30
Automated operating discipline for consistent plant operation
in a large-scale chemical plant – Benefits
Detecting problems the operators may miss;
Eliminating upsets or minimizing the number of upsets to just a few each year;
Catching operator mistakes, specifically on complex alarm cases that include parameters from different process units;
Training new operators on problem detection and corrective actions;
Catching operator mistakes, specifically on complex alarm cases that include parameters from different process units;
Training new operators on problem detection and corrective action;
Fast problem recognition due to reliable soft sensors;
Estimated NPV for one reactor is $xxxxxxx. Leveraged to five more reactors

## Slide 31: Lecture 16 agenda

## Slide 32: Predictive maintenance: Reducing paper machine breaks
Paper machine
Stops after paper machine break
Paper machine breakdowns led to 1.6 hours average loss of production time per day, which amounts to $6–8 million per year for each production line.

## Slide 33: Predictive paper machine breaks: Data collection strategy
Build a fault detection model based on predictive features in yellow color data

## Slide 34: Predictive paper machine breaks: Defining the warning flag threshold
T2 statistics based on 180 inputs
Raises warning flag if > limit (UCL)
Case 1
03/07/17a
Case 2
03/07/17b
Case 3
03/13/17
Normal
operation
Case 4
03/24/17
--180 min
-180 min
Break
Break

## Slide 35: Predictive paper machine breaks: Real-time system operation
Change in lab measurement (cobb/felt top)
Machine health monitor
Crossing red line raises alarm

## Slide 36: Predictive paper machine breaks: Performance tracking
PM2 Stability Application Released
12/15/17
Operator Training
4/4/18
Reduced machine brakes after system in action
Before
After

## Slide 37: Lecture 16 “Applied AI in industry” Summary
The main features in applying AI in manufacturing are: engineers are the
key users, problems are technically-driven, and model deployment is in real-time
The key features of manufacturing data are: most of the data is numeric, well-structured, and generated by sensors
Industry 4.0 includes cyber-physical systems, the Internet of Things, cloud computing and AI
Digital twins are the most used cyber-physical systems
An example of empirical emulators demonstrates an alternative low-cost option to digital twins
Inferential sensors, automating operating discipline, and predictive maintenance are examples of successful AI applications in manufacturing.
The Bottom Line
Applied AI has demonstrated an impressive record of industrial success stories

## Slide 38: Details on this topic are given in the following chapters of “Applying Data Science” book: Chapter 14